## Slide 1: Maritime Distress Intelligence
From a noisy multilingual VHF call to a verified incident and a search plan
Data Science course project
Notes: Open with the one-line promise: a distress call comes in on channel 16, possibly in Hindi, Tamil or Malayalam, over a noisy radio. The system turns it into a structured, explained incident and a search plan in seconds, and the operator verifies everything.

## Slide 2
THE PROBLEM
4
languages on the radio along the Indian coast: English, Hindi, Tamil, Malayalam
0
public labelled VHF distress-call datasets for Indian waters
24 h
a drifting casualty can move 10+ nm; every hour widens the search
Operators must extract who, where, what and how many, under stress, from a few seconds of radio.
Notes: There is no public labelled corpus for this, which is why the project generates its own labelled data and validates on external datasets.

## Slide 3
THE PRODUCT
1
Listens
Whisper ASR with fine-tuned Indic checkpoints
2
Extracts
Vessel, MMSI, position, persons on board, incident type, with evidence
3
Judges
Severity with calibrated probabilities and a 90% set
4
Plans
Drift forecast, search area and fastest assets
The operator verifies every field. The system never dispatches on its own.

## Slide 4
HOW IT WORKS
Audio
VHF channel
simulation
Speech
Whisper +
Indic fine-tunes
Entities
CRF sequence
labelling
Incident
TF-IDF +
logistic regression
Severity
Calibrated,
conformal sets
Drift
Physics +
LightGBM
Assets
Hungarian
assignment
Optional LLM layer Qwen2.5-1.5B fills fields the CRF misses. Every LLM answer must quote the transcript, and our own parsers convert numbers, never the LLM.

## Slide 5
DATA SCIENCE DEPTH
Learning models · 6
Linear-chain CRF (NER)
TF-IDF + logistic regression
Ordinal vs multinomial regression
LightGBM residual model
Whisper transfer learning
Grammar-constrained LLM
Uncertainty · 5
Temperature scaling + ECE
Split conformal prediction
Conformal search radius
Bootstrap confidence intervals
Exact linear SHAP
Simulation · 4
Synthetic data generator
VHF signal processing
Monte Carlo drift
Hungarian assignment
Evaluation design · 5
Leakage-controlled splits
Buoy-grouped cross-validation
Dev / test protocol
Robustness vs ASR noise
Learned CRF/LLM routing
Every technique is evaluated against a baseline on held-out or external data.
Notes: 20 distinct methods. Stress that each has a baseline and a held-out evaluation, not just an implementation.

## Slide 6: Labels we generate, realism we borrow
DATA
20,000
synthetic distress dialogues
Labels sampled before text, so spans are exact
4 languages × 3 caller styles
Held-out vessels, landmarks and phrasings
MARTTS
240 real radio dialogues
test
SeaAlert
1,872 VHF messages + ASR
test
Kathbath
real Indian speech
test
MUSAN
real background noise
train
NOAA drifters
real buoy tracks
train/test
ERA5 + Copernicus
wind and currents
input
MarineCadastre AIS
real vessel speeds
input
GEBCO
bathymetry / land mask
input

## Slide 7: Entities and incidents, on phrasings never seen in training
LANGUAGE UNDERSTANDING
Chart: CRF entity F1 by type
| INCIDENT | MMSI | POB | POSITION | VESSEL | VESSEL TYPE
F1 | 0.78 | 0.85 | 0.95 | 0.98 | 0.89 | 0.88
0.89
entity micro-F1 (95% CI 0.885–0.898)
0.89
incident macro-F1, vs 0.80 for keyword rules
Unseen vessel names: a shape feature stops the CRF memorising names (66% → 99.6% exact).

## Slide 8: Probabilities you can trust, sets that admit doubt
SEVERITY AND TRUST
81%
severity accuracy vs 46% majority baseline
89%
conformal 90% sets hit the true severity (mean size 1.40)
Chart: Calibration error (lower is better)
| Uncalibrated | Temperature-scaled
ECE | 0.092 | 0.073
Explained
fire
man overboard
capsizing
n incident types
flooding
Linear SHAP: weights that raise HIGH/CRITICAL

## Slide 9: Where the severity model goes wrong
SEVERITY DIAGNOSTICS
Predicted
True
LOW
MODERATE
HIGH
CRITICAL
LOW
182
96%
2
1%
6
3%
0
0%
MODERATE
3
1%
288
90%
29
9%
0
0%
HIGH
15
2%
45
5%
843
92%
14
2%
CRITICAL
11
2%
12
2%
248
43%
303
53%
43% of CRITICAL calls are rated HIGH: the costly error
Chart: Reliability diagram: accuracy per confidence bin
| 0.3–0.4 | 0.4–0.5 | 0.5–0.6 | 0.6–0.7 | 0.7–0.8 | 0.8–0.9 | 0.9–1
Perfect calibration | 0.35 | 0.45 | 0.55 | 0.65 | 0.75 | 0.85 | 0.95
Uncalibrated | 0.38 | 0.59 | 0.63 | 0.75 | 0.69 | 0.67 | 0.93
Temperature-scaled | 0.5 | 0.74 | 0.66 | 0.68 | 0.81 | 0.97 | 1
Conformal sets cover 99% of HIGH but only 68% of CRITICAL calls. Next: class-conditional conformal.

## Slide 10: Fine-tuned Whisper cuts noisy-speech errors in half
SPEECH RECOGNITION
Chart: Word error rate, real speech through a simulated VHF channel
| Hindi | Tamil | Malayalam
Whisper-small | 0.73 | 0.73 | 1
Fine-tuned Indic Whisper | 0.28 | 0.37 | 0.23
73% → 28%
Hindi word errors over radio noise
94% → 78%
caller WER on our 24 synthetic TTS calls; CER 76% → 77%, so synthetic audio is the bottleneck
AI4Bharat Kathbath, 8 speakers per language (Malayalam 2). No training run: published checkpoints, measured on our channel.

## Slide 11: A small open LLM, kept honest by a grounding guard
LLM EXTRACTION
Chart: Field accuracy on SeaAlert, noisiest ASR transcripts
| Vessel | Position | Persons on board | MMSI
CRF only | 0.03 | 0.55 | 0.55 | 0
CRF + LLM, routing learned on dev | 0.27 | 0.64 | 0.69 | 0.09
123
LLM answers blocked: quote not in the transcript or not a valid value
1.5B
parameters, 4-bit, laptop CPU, output constrained to a JSON schema
Learned on dev data: vessel: LLM · mmsi: LLM · position: CRF · POB: LLM

## Slide 12: Physics plus machine learning, tested on real ocean buoys
DRIFT FORECASTING
Chart: Mean position error after drifting (nautical miles)
| 6 h | 12 h | 24 h
Object stays put | 2.79 | 5.48 | 10.7
Physics | 2.4 | 4.68 | 9.08
Physics + LightGBM | 2.41 | 4.66 | 8.89
17%
better than 'object stays put' at 24 h
+2.1%
LightGBM over physics at 24 h
95% CI 0.6% to 3.6%
1600 start points from 11 NOAA buoys · cross-validated by buoy · conformal 90% search radius

## Slide 13: Trained on synthetic data, tested on real radio dialogues
EXTERNAL VALIDATION
Chart: MARTTS held-out test dialogues (DLR, n = 177)
| Vessel name | MMSI | Position ≤ 1 nm
Zero-shot | 0 | 0.44 | 0
After fixes found on the dev split | 0.37 | 0.82 | 1
62% → 2%
routine calls wrongly rated HIGH or CRITICAL
0.56
SeaAlert category F1 at heavy ASR noise, vs 0.42 published logistic regression
Fixes were made on a dev split only; test dialogues were scored, never inspected.

## Slide 14: What a real deployment would still need
HONEST LIMITS AND NEXT STEPS
Limits
Labels are synthetic; Indic phrasing needs native-speaker review
Only 11 buoys with current data limit the drift model
Small external samples (24–177 items) give wide intervals
Kathbath may overlap the checkpoints' training data
Next steps
Record real calls with consenting operators
LoRA fine-tune Whisper on radio-channel audio
LoRA fine-tune the LLM on our labelled dialogues
Stream live calls through Kafka; real AIS feed

## Slide 15: Live demo
One distress call, end to end: audio, transcript, extraction, severity, drift and dispatch
Thank you · questions welcome